array-gpio
A node.js GPIO control for rapid prototyping and development using a simple modern API.
https://npm.taobao.org/package/array-gpio

Last updated 2 months ago by edolabworks - MIT · Original npm · Tarball

$ cnpm install array-gpio
SYNC missed versions from official npm registry.
array-gpio
A node.js ARM peripherals control for rapid prototyping and development using a simple modern API.
Supports the following ARM peripherals
- GPIO
- PWM
- I2C (master)
- SPI
This module uses a C/C++ addon to access the rpi library using /dev/mem (PWM, I2C, SPI) & /dev/gpiomem (GPIO) for direct register control. You can check the library at https://github.com/EdAlegrid/rpi.
For a quick web control application, check the sample demo at https://github.com/EdAlegrid/PiWebControl.
Compatibility
- Raspberry Pi Models: B+, 2, 3, Zero & Zero W.
- Node.js Versions: 5.x, 6.x, 7.x, 8.x
Note: This module uses the physical pin numbering (P01-P40) from the board header.
Installation
$ npm install array-gpio
Quick Start
Creating an input/output object
Example 1
One momentary switch button connected to pin 11 and one led connected to pin 33.
/* r for raspberry pi */
const r = require('array-gpio');

/* Creating an input object */
let sw = r.Input(11);

/* Creating an output object */
let led = r.Output(33);

/* Monitor input pin for rising edge value changes */
sw.watch('re', function(){ /* press sw button to turn ON the led */
  led.on();
});
Example 2
Two momentary switch buttons connected to pin 11 and 13 and one led connected to pin 33.
/* r for raspberry pi */
const r = require('array-gpio');

/* Using .in() and .out() as shorthand
   for .Input() and .Output() constructor methods */
let sw1 = r.in(11);
let sw2 = r.in(13);
let led = r.out(33);

/* press sw1 to turn ON the led */
sw1.watch('re', function(){
  led.on();
});

/* press sw2 to turn OFF the led */
sw2.watch('re', function(){
  led.off();
});
Using a shared callback function to capture input pin changes.
If you have more than one input object, it might be handy to use a shared callback function for input changes monitoring.
r.watchInput(function(){
  /* Press sw1 to turn ON the led */
  if(sw1.isOn){
    return led.on();
  }
  /* Press sw2 to turn OFF the led */
  if(sw2.isOn){
    return led.off();
  }
});
Example 3
Using parameters in callback function. Following node.js convention, we can pass an error object as 1st parameter and a state value as 2nd parameter to our callback function.
const r = require('array-gpio');

let sw1 = r.in(11);
let led = r.out(33);

sw1.watch( 're', (err, state) => {
  if(err) return console.log('sw1 err', err);
  led.write(state);
});
However, using a callback function without parameters is simplier and should be fine in most cases.
Creating an input/output array objects
If you are comfortable working with arrays and you need to use several input/output objects in your application, you can generate an input/output array objects as shown below.
Example 1
Two momentary switch buttons connected to pin 11 and 13 and two led's connected to pin 33 and 35.
const r = require('array-gpio');

/* By providing more than one pin parameter to Input/Output
   constructor methods, we create an array object. */

let sw = r.Input(11,13);
let led = r.Output(33,35);

/* By default, input/output array objects will be indexed
 * consecutively from 0 to n (total no. of input/output pins).
 *
 * sw[0] - switch button connected to pin 11
 * sw[1] - switch button connected to pin 13
 * led[0] - led connected to pin 33
 * led[1] - led connected to pin 35
 */

/* Using a shared callback function to monitor input changes */
r.watchInput(function(){
  /* Press sw[0] to generate a single pulse on pin 33 */
  if(sw[0].isOn){
    return led[0].pulse(1000); /* pulse width is 1000 ms */
  }
  /* Press sw[1] to generate a single pulse on pin 35 */
  if(sw[1].isOn){
    return led[1].pulse(1000);
  }
});
Using local events to watch/monitor for input changes.
const r = require('array-gpio');

let sw = r.in(11,13);
let led = r.out(33,35);

sw[0].watch('re', () => {
    /* turns ON led[0] after 500 ms delay */
    led[0].delayOn(500, () => {
        led[0].delayOff(1000); /* turns OFF after 1000 ms */
    });
});

/* passing parameters to callback functions */
sw[1].watch('re', (err, state) => {

    if(err) return console.log('sw[1] watch error', err.message);

    /* turns ON led[1] using output write method */
    led[1].write(state, (err) => {

        if(err) return console.log('sw[1] write error', err.message);

        led[1].off(1000); /* turns OFF after 1000 ms */
    });
});
Example 2
Creating array objects using the pin number as index so we can reference each input/output object by its pin number.
const r = require('array-gpio');

let sw = r.in(11,13, {index: 'pin'});
let led = r.out(33,35, {index: 'pin'});

/* Both input/output array objects will be indexed by its pin number.
 *
 * sw[11] - switch button connected to pin 11
 * sw[13] - switch button connected to pin 13
 * led[33] - led connected to pin 33
 * led[35] - led connected to pin 35
 */

r.watchInput(function(){
  if(sw[11].isOn){
    return led[33].on();
  }
  if(sw[13].isOn){
    led[33].off();
    return led[35].pulse(1000);
  }
});
Example 3
Two momentary switch buttons connected to pin 11 and 13 and six led's connected to pin 33, 35, 37, 36, 38 and 40.
const r = require('array-gpio');

let input = r.in(11,13);
let output = r.out(33,35,37,36,38,40);

/* turn ON led's sequentially */
function LedOn(){
  let t = 50; /* ON time delay in ms */
  for (let x in output){
    t += 50;
    output[x].on(t);
  }
}
/* turn OFF led's sequentially */
function LedOff(){
  let t = 50; /* OFF time delay in ms */
  for (let x in output){
    t += 50;
    output[x].off(t);
  }
}

r.watchInput(function (){
  if(input[0].isOn){
    LedOn(); /* turns ON the output leds sequentially */
  }
  else if(input[1].isOn){
    LedOff(); /* turns OFF the output leds sequentially */
  }
});
API
Input(pin1, pin2, ... , pinN)
or
in(pin1, pin2, ... , pinN)
input object constructor
Sets a GPIO pin or group of GPIO pins as input object.
Choose your pin based on the physical pin numbering (P01-P40) from the board header.
Returns an input object or an array object if more than one pin parameter is used.
/* creates a single input object */
var sw1 = r.Input(11);
/* creates an array input object */
var input = r.Input(11,13,15,19});
By default, array object will be indexed consecutively (0 to n) as element of the returned array object.
If you want to use the pin number as index, you can use the following options.
var input = r.Input(11,13,15,19, {index: 'pin'});
or
var input = r.Input({pin:[11,13,15,19], index:'pin'});
You can set as many input pins as you can. You are only limited by how much GPIO pins are available on your Raspberry Pi.
Using object literal as pin argument
var arg = {pin:[pin1, pin2, pin3 ... pinN]};
Input(arg)
Example
let arg = {pin: [11, 13, 15]};

var input = r.Input(arg);
state
input/output property
Reads the current logical condition of any input/output object at any given point in your application during runtime.
Returns true if the object is in high or ON state condition.
Otherwise returns false for low or OFF state condition.
Example 1
const r = require('array-gpio');

let sensor = r.in(11);

/* returns the current state of sensor object */
console.log(sensor.state);
Example 2
const r = require('array-gpio');

let sw = r.in(11);
let led = r.out(33);

sw.watch(function(){
  if(sw.state && led.state === false){

  console.log(sw.state); // true
  console.log(led.state); // false

  led.on();

  console.log(sw.state); // true
  console.log(led.state); // true
  }
});
isOn and isOff
input/output property
Similar to state property but with explicit context.
isOn returns true if state is true, otherwise it returns false.
isOff returns true if state is false, otherwise it returns false.
Example 1
const r = require('array-gpio');

let sw1 = r.in(11);
let sw2 = r.in(13);
let led = r.out(33);

r.watchInput(() => {
  /* turns on led if sw1 is ON and if led is OFF */
  if(sw1.isOn && led.isOff){
    return led.on();
  }
  /* turns off led if sw2 is ON and if led is ON */
  if(sw2.isOn && led.isOn){
    return led.off();
  }
});
read([callback])
input/output method
The conventional way of getting the current state of any input/output object.
Returns 1 for ON or high state and 0 for OFF or low state.
callback If provided, it will be executed after the state value is obtained.
/* r for raspberry pi */
const r = require('array-gpio');

let sw = r.Input(11);
let solenoid = r.Output(35);

sw.watch(function(){
  let status = sw.read(() => {
    if(status === 1)
      solenoid.on(50);
    else
      solenoid.off();
  });
});
watch (edge, callback)
input method
Use it to listen for input pin value changes.
You can listen for rising or falling edge events or both.
edge
're' or 1 - Enable rising edge (high transition) event detection.
'fe' or 0 - Enable falling edge (low transition) event detection.
'both' - Enable both rising and falling edge event detection.
or
By not providing an edge parameter, both rising and falling edge detection will be enabled.
callback parameter will be executed when input changes or events are detected.
const r = require('array-gpio');

let sw = r.in(11);

function pinEvent(){
  console.log('pin event detected');
}

// enable rising edge detection
sw.watch('re', pinEvent);
// or
sw.watch(1, pinEvent);

// Enable falling edge detection
sw.watch('fe', pinEvent);
// or
sw.watch(0, pinEvent);

// edge parameter is not provided,
// both rising and falling edge detection will be enabled
sw.watch(pinEvent);
Example 1
const r = require('array-gpio');

let sw1 = r.in(11);
let led = r.out(33);

/* Pressing sw1 button will turn ON the led. */
sw1.watch( 're', (err, state) => {
  if(err) return console.log('sw1 err', err);
  led.write(state);
});
Example 2
const r = require('array-gpio');

let sw = r.Input(11, 13);
let led = r.Output(33, 35);

/* sw[0] will listen both for rising and falling input pin value changes */
/* Pressing and releasing button switch sw[0], led[0] and led[1] will turn ON and OFF respectively */
sw[0].watch(function(){
    console.log('sw[0] input pin event detected');
    if(led[0].isOff){
      led[0].on();
    }
    if(led[1].isOn){
      led[1].off();
    }
});

/* sw[0] will listen only for falling input pin value changes or when switch button is released */
sw[1].watch(0, function() {
    console.log('sw[1] input pin event detected');
    if(led[0].isOn){
      led[0].off();
    }
    if(led[1].isOff){
      led[1].on();
    }
});
clearEvent()
input method
Input stops listening to any input events.
const r = require('array-gpio');

/* using one button switch */
let sw = r.Input(11);

sw.watch(1, function(){
  console.log("I'm only a one-time event");
  sw.clearEvent();
});
Using clearEvent() to debounce a switch.
const r = require('array-gpio');

let sw1 = r.Input(11);
let sw2 = r.Input(13);
let led = r.Output(33);

/* debouncing sw1 */
function OnEvent(){
  console.log('led is ON');
  led.on();
  sw1.clearEvent();
}

/* ON switch */
sw1.watch(1, OnEvent);

/* OFF switch */
/* OFF switch */
sw2.watch(1, function(){
  led.off();
  console.log('led is OFF');
  sw1.watch(1, OnEvent);
});
watchInput (callback)
main module object method
It will listen both for rising and falling edge input pin events.
callback parameter is shared among all input objects created.
To capture events from a particular pin, you can check the input object's state or isOn property.
Example
const r = require('array-gpio');

let sw = r.Input(11, 13, 15, {index:'pin'});
let led = r.Output(33, 35, {index:'pin'});

r.watchInput(function (){
  if(sw[11].isOn){ /* if sw[11] is ON, led[33] will turn ON */
    return led[33].on();
  }
  if(sw[13].isOn){ /* if sw[13] is ON, led[35] will turn ON */
    return led[35].on();
  }
  if(sw[15].isOn){ /* if sw[15] is ON, both led[33] and led[35] will turn OFF */
    led[33].off();
    return led[35].off();
  }
});
Passing an error object to callback function to capture internal errors.
const r = require('array-gpio');

let sw1 = r.in(11);
let sw2 = r.in(13);
let led1 = r.out(33);
let led2 = r.out(35);

r.watchInput((err) => {

  if(err) return console.log('watchInput error', err.message);

  if(sw1.isOn){
    led1.on();
    return led2.off();
  }
  if(sw2.isOn){
    led2.on();
    return led1.off();
  }
});
Output(pin1, pin2, pin3 ... pinN)
or
out(pin1, pin2, pin3 ... pinN)
output object constructor
Sets a GPIO pin or group of GPIO pins as output object.
Choose your pin based on the physical pin numbering (P01-P40) from the board header.
Returns an output object using a single pin parameter or an array object using more than one pin as parameter
/* creates a single output object */
var led = r.Output(11);
/* creates an array output object */
var output = r.Output(11,13,15,19});
Similar to Input(), returned array object will be indexed consecutively.
If you want to use the pin number as index, use the following options.
var output = r.Output(33,35,36,37, {index: 'pin'});
or
var output = r.Output({pin:[33,35,36,17], index:'pin'});
Similar to Input(), you can set as many output pins as you can.
Using object literal as pin argument
Output(arg)
var arg = {pin:[pin1, pin2, pin3 ... pinN]};
const r = require ('array-gpio');

let arg = {pin:[33,35,37,36,38,40]};

var actuator = r.Output(arg);
on([t]) and off([t])
output method
Turns ON and OFF an output object.
t is an optional time delay in milliseconds. Output object will turn ON or OFF after the expiration of time delay.
Example
const r = require('array-gpio');

let sw = r.Input(11,13);
let actuator = r.Output(33,35);

r.watchInput(() => {
  if(sw[0].isOn && actuator[0].isOff){
    actuator[0].on(200); /* turns ON after 200 ms delay */
    actuator[1].on(); /* turns ON immediately */
  }
  else if(sw[1].isOn && actuator[1].isOn){
    actuator[0].off(50); /* turns OFF after 50 ms delay */
    actuator[1].off(); /* turns OFF immediately */
  }
});
write(value[ ,callback])
output method
The conventional way of turning ON and OFF an output object.
value - control bit number.
1 or true - ON or high state
0 or false - OFF or low state
Optional callback parameter will be executed immediately if provided.
Example
const r = require('array-gpio');

const sw = r.Input(11,13);
const actuator = r.Output(33,35);

let sw1 = sw[0];
let sw2 = sw[1];

let motorA = actuator[0];
let motorB = actuator[1];

r.watchInput(() => {
  if(sw1.read() === 1){
    motorA.write(1, function(){
      if(motorB.read() === 0)
      motorB.write(1);
    });
  }
  if(sw2.read() === 1){
    motorA.write(0, function(){
      if(motorB.read() === 1)
      motorB.write(0);
    });
  }
});
delayON(t [,callback]) and delayOFF(t [,callback])
or
delayOn(...) and delayOff(...)
output method
Lets you turn ON and OFF an output object with a delay time.
t is the required time delay in milliseconds. Output object will turn ON or OFF after the expiration of time delay.
Optional callback parameter will be executed when time delay expires.
Example
const r = require('array-gpio');

const sw = r.in(11,13);
const actuator = r.out(33,35);

r.watchInput(() => {
 if(sw[0].state && actuator[0].state === false){
  /* actuator[0] will turn ON after 1 sec */
  actuator[0].delayON(1000, function(){
    console.log('actuator is ON!'); /* prints out after 1 sec */
  });
  console.log('turning ON actuator ...'); /* prints out immediately */
 }
 else if(sw[1].state && actuator[0].state){
  /* actuator[0] will turn OFF after 1.5 secs */
  actuator[0].delayOFF(1500, function(){
    console.log('actuator is OFF!'); /* prints out after 1.5 secs */
  });
  console.log('turning OFF actuator ...'); /* prints out immediately */
 }
});
pulse(pw [,callback])
output method
Generates a single square wave pulse with a duration of pw ms.
pw is the required pulse width or time duration of the pulse.
Optional callback parameter will be executed when time duration expires.
Example
const r = require('array-gpio');

let sw = r.in(11,13);
let actuator = r.out(33,35);

r.watchInput(() => {
  /* starts a single pulse w/ a duration of 1 sec */
  if(sw[0].isOn && actuator[0].isOff){
    return actuator[0].pulse(1000);
  }
  /* starts a single pulse w/ a duration of 2 secs */
  if(sw[1].isOn && actuator[1].isOff){
    console.log('start of pulse');
    return actuator[1].pulse(3000, () => {
      console.log('end of pulse');
    });
  }
});
loop(cs, T, callback)
output method
This is a utility function for general purpose looping operations.
It is attached to an output object as a property method but it is totaly independent from its GPIO operations. So you can continue using the output object for other purposes while using the loop utility.
It is not very different from setInterval() function. However, it has some internal flags to prevent a race condition.
cs is a control flag.
Use 1 to start the looping operation along with the other arguments.
Use 0 or without any arguments to stop.
T (ms) is the time interval of the looping operation. Minimum is 10 ms.
callback function will be executed at the end of time interval. This is the task or process you want to loop or cycle continously.
The total elapsed time of the process must be accounted for or determined if you are using a lot of time delays in your I/O operations.
Example
const r = require('array-gpio');

const input = r.Input(11,13);
const led = r.Output(33,35,37,36,38,40);

let start = input[0];
let stop = input[1];

// using the loop utility from led[0]
// without affecting its led ON/OFF operation
let ledSequence = led[0];

// turn ON and OFF led's sequentially
// total elapsed time is 700 ms
let ledOnOff = () => {
  let t = 0;
  for (let x in led){
    t += 100;
    led[x].delayOn(t, () => console.log('led[' + x + '] is ON'));
    led[x].delayOff(t + 400, () => console.log('led[' + x + '] is OFF'));
  }
};

r.watchInput(() => {
  if(start.isOn){
    // start the ledOnOff sequence
    return ledSequence.loop(1, 1000, ledOnOff);
  }
  if(stop.isOn){
    // stop the ledOnOff sequence
    return ledSequence.loop();
  }
});

var appExitProcess = () => {
  console.log('closing all I/O objects');
  for(let x in input){
    input[x].close();
  }
  for(let x in led){
    led[x].close();
  }
}

// using Ctrl-C for app exit
process.on('SIGINT', () => {
  appExitProcess();
  process.exit(0);
});
pin
input/output property
Returns the GPIO pin used from your input and output objects.
Example
const r = require('array-gpio');

let sw = r.Input(11);
let led = r.Output(33);

console.log(sw.pin); // 11
console.log(led.pin); // 33
close()
input/output method
Closes any input/output object.
Example 1
const r = require('array-gpio');

let sw = r.Input(11);
let led = r.Output(33);

sw.close();
led.close();
Example 2
const r = require('array-gpio');

let input = r.Input(11, 13);
let output = r.Output(33, 35);

function appExitProcess(){
  console.log('closing all I/O objects');
  for(let x in input){
    input[x].close();
  }
  for(let x in output){
    output[x].close();
  }
}

// using Ctrl-C for app exit
process.on('SIGINT', function (){
  appExitProcess();
  process.exit(0);
});
setR(intR)
input method
Sets or changes input internal resistor using either pull up or pull down.
intR
'pu' or 1 - Enable pull up resistor.
'pd' or 0 - Enable pull down resistor.
If no parameter is provided, no internal resistor will be used.
Example
const r = require('array-gpio');

let sw = r.Input(11,13,15);

// using pull up resistor
sw[0].setR('pu');
// using pull down resistor
sw[1].setR(0);
// no internal resistor
sw[2].setR();

PWM(pin)
PWM object constructor
pin
Use PWM hardware peripherals to generate square-wave pulses for selected physical pin numbers 12, 32, 33 and 35 using its alternate function.
Channel 1 - pins 12 and 32.
Channel 2 - pins 33 and 35.
You can only control 2 peripherals independently, one from channel 1 and one from channel 2. If both peripherals are from the same channel, you can control both channels using only the control values (setRange and setData) from one of the peripherals.
Check the available pins based on your Raspberry pi models.
Requires root access to run your application.
setClockFreq(div)
div The the divisor value to calculate the desired clock frequency from a fixed oscillator of 19.2 MHz.
(0 to 4095)
freq = 19200000/div
setRange(range)
Sets the period T of the pulse.
setData(data)
Sets the pw (pulse width) of the pulse.
stop()
Stop the pulse generation of the system 19.2 MHz clock oscillator.
You can restart the pulse generation anytime using the pulse() or setData() function.
close()
Stop and disable PWM. Returns back the pin used for GPIO use.
Example 1
/* Connect an led to pin 12. */

/* r for raspberry pi */
const r = require('array-gpio');

/* start PWM using pin 12 */
var pwm = r.PWM(12);

/* set clock frequency using a div value of 1920 */
pwm.setClockFreq(1920); // sets clock freq to 10kHz or 0.1 ms time resolution for T and pw

/* set period (T) of the pulse */
pwm.setRange(1000); // 1000 x 0.1 ms = 100 ms (actual period T)

/*
 * set pw (pulse width) of the pulse and start the pulse generation for 2 seconds
 *
 * The led attached to pin 12 should blink for 2 seconds
 */
pwm.setData(100); // 100 x 0.1 ms = 10 ms (actual pw)

/* stop PWM and return pin 12 to GPIO input mode */
setTimeout(function(){

  pwm.stop();
  pwm.close();

}, 2000);

PWM(pin, freq, T, pw)
PWM object constructor
A quick way to start PWM with predefined clock frequencies.
pin
Choose from channel 1 pins (12, 32) or channel 2 pins (33, 35).
freq (kHz)
Choose from 3 predefined clock oscillator frequency that will provide different time resolutions for your T (period) and pw (pulse width).
10 kHz -> 0.1 ms
100 kHz -> 0.01 ms
1000 kHz -> 0.001 ms or 1 uS (microsecond)
T (ms) is the initial cycle period T of the pulse.
pw (ms) is the initial pulse width of the pulse.
The ratio of pw over T is the pulse duty cycle (pw/T) x 100%.
pulse([pw])
Start the pulse generation or create a new pulse using the pw parameter provided. If pw is not provided, it will use the initial pw from the PWM constructor and start the pulse generation.
pw (ms) is the pulse width that will be used to generate a new pulse.
You can change the period T using setRange() and pw using setData() or pulse() function at anytime in your application. However, T is usually fixed while changes in pw controls the behaviour of your motor device.
Example 2
/* Using a generic micro servo motor (~4.8 to 6.0 V)
 *
 * T period = 20 ms
 *
 * pw (pulse width) needed for various servo positions
 *
 * pw = 1.0 ms - pos 1, home position
 * pw = 1.5 ms - pos 2, rotates 40 degrees cw (clockwise) from pos 1
 * pw = 2.0 ms - pos 3, rotates 80 degress cw from pos 1
 * pw = 2.5 ms - pos 4, rotates 120 degress cw from pos 1
 *
 */

const r = require('array-gpio');

var pin = 33; /* channel 2, alt-function 0 */
var freq = 10; /* 10 kHz provides 0.1 ms time resolution */
var T = 200; /* 200 x 0.1 ms = 20 ms */
var pw = 10; /* 10 x 0.1 ms = 1.0 ms, home position */

/* start PWM and initialize with above details */
var pwm = r.PWM(pin, freq, T, pw);

/* create four push buttons sw[0], sw[1], sw[2] and sw[4] */
const sw = r.Input(11,13,15,19);

r.watchInput(() => {
  /* Press sw[0] button to rotate the servo motor to pos 1 or home position */
  if(sw[0].isOn){
    pwm.pulse(10); // 1.0 ms pw
  }
  /* Press sw[1] button to rotate to pos 2 */
  else if(sw[1].isOn){
    pwm.pulse(15); // 1.5 ms pw
  }
  /* Press sw[2] button to rotate to pos 3 */
  else if(sw[2].isOn){
    pwm.pulse(20); // 2.0 ms pw
  }
  /* Press sw[3] button to rotate to pos 4 */
  else if(sw[3].isOn){
    pwm.pulse(25); // 2.5 ms pw
  }
});

const appExitProcess = () => {
 console.log('closing all sw and pwm objects');
  for(let x in sw){
    sw[x].close();
  }
  pwm.close();
  process.exit(0);
}

process.on('SIGINT', () => {
  console.log('\napp terminated using Ctrl-C');
  appExitProcess();
});

I2C()
Start I2C operations. Set pins 03 (SDA) and 05 (SCL) to alternate function 0 (ALT0) for I2C single master serial data transfer operations.
Requires root access.
begin()
Enable or restart I2C interface at anytime in your application. However, it is not necessary when using the I2C() constructor.
end()
End I2C operations. I2C pins 03 (SDA) and 05 (SCL) are returned to GPIO input mode.
setTransferSpeed(baud)
Sets the I2C clock frequency by converting the baud parameter to the equivalent I2C clock divider value.
setClockFreq(div)
Sets the I2C clock speed based on the div divisor value. Check values below.
div = 2500 => 10us	=> 100 kHz
div = 626 => 2.504us	=> 399.3610 kHz
div = 150 => 60ns	=> 1.666 MHz (default at reset)
div = 148 => 59ns	=> 1.689 MHz
selectSlave(addr)
Sets the I2C slave address.
addr The I2C slave address.
write(wbuf, len)
Write a number of bytes to the currently selected I2C slave.
wbuf Buffer of bytes to write/send.
len Number of bytes to write/send.
read(rbuf, len)
Read a number of bytes from the currently selected I2C slave.
rbuf Buffer of bytes to read/receive.
len Number of bytes to read/receive.
/* Using MCP9808 Temperature Sensor */

const r = require('array-gpio');

var i2c = r.I2C();

/* set data transfer speed to 400 kHz */
i2c.setTransferSpeed(400000);

/* MCP9808 device address */
let slave = 0x18;

/* access MCP9808 device */
i2c.selectSlave(slave);

/* setup write and read data buffer */
const wbuf = Buffer.alloc(16); // write buffer
const rbuf = Buffer.alloc(16); // read buffer

/* accessing the internal 16-bit manufacturer ID register within MCP9808 */
wbuf[0] = 0x06; // address of manufacturer ID register
i2c.write(wbuf, 1);

/*
 * read content of 16-bit manufacturer ID register (should be 0x54 as per datasheet)
 * reads upper byte (rbuf[0]) and lower byte (rbuf[1]), ID value is on the lower byte
 */
i2c.read(rbuf, 2);

console.log('MCP9808 ID: ', rbuf[1].toString(16)); // convert ID to hex value

/* Based on MCP9808 datasheet, compute the temperature data as follows */
function getTemp(){

  /* variable for temperature data */
  let Temp;

  let UpperByte = rbuf[0];
  let LowerByte = rbuf[1];

  UpperByte = UpperByte & 0x1F; // Clear flag bits

  // Temp < 0°C
  if ((UpperByte & 0x10) == 0x10){
UpperByte = UpperByte & 0x0F; // Clear SIGN
Temp = 256 - ((UpperByte * 16) + (LowerByte / 16));

  // Temp > 0°C
  }else {
Temp = ((UpperByte * 16) + (LowerByte / 16));
  }

  /* Print out temperature data */
  console.log('Temp: ', Temp);

}

/* get temperature readings every 2 seconds */
setInterval( function(){

  /*
   * accessing the internal 16-bit configuration register within MCP9808
   * You can skip accessing this register using default settings
   */
  wbuf[0] = 0x01; // address of configuration register
  /* change content of configuration register */
  wbuf[1] = 0x02; // register upper byte, THYST set with +1.5 C
  wbuf[2] = 0x00; // register lower byte (power up defaults)
  i2c.write(wbuf, 3);

  /* accessing the internal 16-bit ambient temp register within MCP9808 */
  wbuf[0] = 0x05; // address of ambient temperature register
  i2c.write(wbuf, 1);

  /* read content of ambient temp register */
  i2c.read(rbuf, 2); // reads UpperByte and LowerByte

  /* get temperature data and print out the results */
  getTemp();

}, 2000);

process.on('SIGINT', function (){
  console.log('\napp terminated using Ctrl-C');
  i2c.end();
  process.exit(0);
});

SPI()
Switches RPi SPI0 pins 19 (MOSI), 21 (MISO), 23 (CLK), 24 (CE0) and 26 (CE1) to alternate function ALT0 for SPI interface use.
Requires root access.
setClockFreq(div)
Sets SPI clock frequency using a divisor value.
Specifies the divisor used to generate the SPI clock frequency. Figures below show the div and clock frequency generated. Clock is based on nominal core clock rate of 250MHz on RPi1 and RPi2, and 400MHz on RPi3.
div The SPI divisor to generate the SPI clock frequency.
SPI div 2048 = 122.0703125kHz on Rpi2, 195.3125kHz on RPI3
SPI div 1024 = 244.140625kHz on Rpi2, 390.625kHz on RPI3
SPI div 512 = 488.28125kHz on Rpi2, 781.25kHz on RPI3
SPI div 256 = 976.5625kHz on Rpi2, 1.5625MHz on RPI3
SPI div 128 = 1.953125MHz on Rpi2, 3.125MHz on RPI3 (default)
SPI div 64 = 3.90625MHz on Rpi2, 6.250MHz on RPI3
SPI div 32 = 7.8125MHz on Rpi2, 12.5MHz on RPI3
SPI div 16 = 15.625MHz on Rpi2, 25MHz on RPI3
SPI div 8 = 31.25MHz on Rpi2, 50MHz on RPI3
chipSelect(cs)
cs = 0, Chip Select 0
cs = 1, Chip Select 1
cs = 2, Chip Select 2
cs = 3, No Chip Select
cs Sets the chip select pin(s). When a data transfer is made, the selected pin(s) will be asserted or held in active state (usually active low) during the transfer.
setCSPolarity(cs, active)
cs The chip select pin you want to change the active state.
active Change the active state of the pin either active low 0 or high 1.
setDataMode(mode)
Sets the SPI data mode. Sets the clock polariy and phase.
mode = 0, CPOL = 0, CPHA = 0
mode = 1, CPOL = 0, CPHA = 1
mode = 2, CPOL = 1, CPHA = 0
mode = 3, CPOL = 1, CPHA = 1
mode Choose one of SPI mode above.
transfer(wbuf, rbuf, len)
Transfers any number of bytes to and from the currently selected SPI slave. Selected CS pins (as previously set by chipSelect) will be held in active state during the transfer.
The data read from the slave is placed into rbuf (rbuf must be at least len bytes long). Uses polled transfer as per section 10.6.1 of the BCM 2835 ARM Peripherals manual.
wbuf Buffer of bytes to write/send.
rbuf Buffer of bytes to read/receive.
len Number of bytes to send/receive.
write(wbuf, len)
Write a number of bytes to the currently selected SPI slave.
Asserts the currently selected CS pins (as previously set by chipSelect) during the transfer.
wbuf Buffer of bytes to write/send to slave.
len Number of bytes to write/send to slave.
read(rbuf, len)
Read a number of bytes from the currently selected SPI slave.
rbuf Buffer of bytes to read/receive from slave.
len Number of bytes to read/receive from slave.
begin()
Enable or restart SPI interface at anytime in your application. However, it is not necessary when using the SPI() constructor.
end()
End SPI operations. SPI0 pins 19 (MOSI), 21 (MISO), 23 (CLK), 24 (CE0) and 26 (CE1) are returned to GPIO input mode.
Example
/* Using MCP3008 10-bit A/D Converter Chip */

/*
 * VDD and Vref are connected to Raspberry Pi 3.3 V
 * Channel 0 (pin 1) will be used for analog input voltage using single-ended mode
 * Since Vref is set to 3.3 V, max. analog input voltage
 * should not be greater than 3.3 V
 *
 * Read the MCP3008 datasheet on how to configure the chip for more details
 */

const r = require('array-gpio');

var spi = r.SPI();

spi.setDataMode(0);
spi.setClockFreq(128);
spi.setCSPolarity(0, 0);
spi.chipSelect(0);

/* setup write and read data buffer */
const wbuf = Buffer.alloc(16); // write buffer
const rbuf = Buffer.alloc(16); // read buffer

/* configure the chip to use CH0 in single-ended mode */
wbuf[0] = 0x01; // start bit
wbuf[1] = 0x80; // using channel 0, single ended
wbuf[2] = 0x00; // don't care data byte as per datasheet
spi.write(wbuf, 3); // write 3 bytes to slave

/* alternative way to write and read to a slave at the same time */
//spi.transfer(wbuf, rbuf, 3); // 3 bytes will be sent to slave and 3 bytes to read

spi.read(rbuf, 3); // read 3 bytes from slave
/* read A/D conversion result */
/* the 1st byte received through rbuf[0] will be discarded as per datasheet */
var data1 = rbuf[1] << 8; // 2nd byte, using only 2 bits data
var data2 = rbuf[2];	// 3rd byte, 8 bits data
var value = data1 + data2; // combine both data to create a 10-bit digital output code

console.log("* A/D digital output code: ", value);

/* compute the output voltage */
var vout = (value * 3.3)/1024;

console.log("* A/D voltage output: ", vout);

spi.end()